## Slide 1: Lab 1: Printed Circuit Boards: Layers, Layers, Layers

## Slide 2: Eagle Trick: The Command Line
You can type commands to Eagle. For some things it’s a huge help
Type “help <command>” to get help
There’s a command for each of the tools in the tool palette.
Useful commands for routing
  Auto – run the auto router
  Ripup – unroute signals
  Show – Highlight a net or part

## Slide 3: PCBs are Made of Layers
Silkscreen – documentation labels
Metal – for making wires
Dialectric – insulation and structure
Solder mask – protective outer coating

## Slide 4: Metal Layers
The Metal layers for several components
  Conductive “traces” to connect components
  Pads for attaching/connecting components
N-layer boards have N metal layers
  N usually is 2,4,...
  Fewer layers  cheaper
Top and bottom layers are for mounting components and routing traces
Internal layers can serve several purposes
  Ground and power planes
  Other signal planes
  Internal routing layers

## Slide 5: Metal Layers (cont.)
Thickness is measured in oz per square foot.
Standard copper is 1oz
  About 0.034 mm
Thicker metal layers can carry more current

## Slide 6: Dielectric
The dielectric in the insulator between metal layers
Most PCBs use FR4
  “glass reinforced epoxy laminate”
  i.e., fancy fiberglass
  “FR” means “flame retardant”
Other specialized dielectrics are are available
  To support high speed circuits
  To manage thermal expansion

## Slide 7: Solder Mask
The solder masking is a polymer (plastic) coating on the top and bottom of the board
Solder does not adhere to it.
It serves several needs
  Protects the top and bottom metal from oxidation.
  Helps prevent solder bridges

## Slide 8: Silkscreen
It’s an opaque (usually) white epoxy or polymer
It provides documentation and markings
  References designators
  Part outlines
  Logos
  Serial numbers etc.

## Slide 9: Making Connections Between Layers
Plated holes connect metal layers.
  Drill a hole
  Electroplate it with copper
The plating attaches to metal that the hole passes through

## Slide 10: Pads and Vias
Vias are electrical connections
  Usually very small.
Through hole pads accommodate through-hole parts
Even larger, mounting holes are possible

## Slide 11: Designing Through-hole Pads
The diameter of the hole is smaller than the drilled hole
  You need to add about 0.1-0.3 mm to the desired, plated internal diameter to get the drill diameter
More here: http://goo.gl/NzcY2W

## Slide 12: Lots of Choices, in Theory
There are many, many choices when designing a PCB
We will get to make very few of them
Cheap, quickturn PCB manufacturers provide a standard setup. E.g.:
  FR4
  1oz copper
  2 or 4 layers

## Slide 13: Resources
White paper about board stackups
  www.icd.com.au/articles/Stackup_Planning_AN2011_2.pdf
Videos of PCB Manufacturing
  This one is very good and really thorough, but it’s too long to watch in class.
  https://www.youtube.com/playlist?list=PL8zP8UuDk8a0ZNWiteC-7PHx1HCeBY0qB

## Slide 14: Steps for Designing PCBs
Create/acquire a library of components
Assemble your schematic
Lay out the board
Perform design checks
Generate CAM files
Perform more design checks
Submit for manufacturing

## Slide 15: Units
Units
  In almost all cases, we will use mm in this class.
  1mm is about 40mils (39.3700787, actually)
  1in is 25.4 mm.
  Keep an eye on your units.
Exceptions
  Lots of tutorials, documents, etc. use mils (1/1000 of an inch) or inches.
  Breadboards and headers are typically 0.1” spacing (2.54mm)

## Slide 16: Designing with Layers
Eagle (and other board design tools) use layers to specify different types of information about a board. E.g:
  Where wires should go on each physical layer
  Where wires should not go on each physical layer
  Documentation
  Mechanical information
Eagle defines 52 layers by default
‘t’ prefix means top.
‘b’ prefix means bottom (displayed mirrored)

## Slide 17: Eagle Layers
Top | Tracks, top side |  | 27 | tValues | Component VALUE, top side |  | 
Route2 | Inner layer |  | 28 | bValues | Component VALUE, bottom side |  | 
Route3 | Inner layer |  | 29 | tStop | Solder stop mask, top side (gen. autom.) |  | Design
Route4 | Inner layer |  | 30 | bStop | Solder stop mask, bottom side (gen. Autom.) |  | Documentation
Route5 | Inner layer |  | 31 | tCream | Solder cream, top side |  | Tool guidance
Route6 | Inner layer |  | 32 | bCream | Solder cream, bottom side |  | 
Route7 | Inner layer |  | 33 | tFinish | Finish, top side |  | 
Route8 | Inner layer |  | 34 | bFinish | Finish, bottom side |  | 
Route9 | Inner layer |  | 35 | tGlue | Glue mask, top side |  | 
Route10 | Inner layer |  | 36 | bGlue | Glue mask, bottom side |  | 
Route11 | Inner layer |  | 37 | tTest | Test and adjustment information, top side |  | 
Route12 | Inner layer |  | 38 | bTest | Test and adjustment inf., bottom side |  | 
Route13 | Inner layer |  | 39 | tKeepout | Restricted areas for components, top side |  | 
Route14 | Inner layer |  | 40 | bKeepout | Restricted areas for components, bottom s. |  | 
Route15 | Inner layer |  | 41 | tRestrict | Restricted areas for copper, top side |  | 
Bottom | Tracks, bottom side |  | 42 | bRestrict | Restricted areas for copper, bottom side |  | 
Pads | Pads (through-hole) |  | 43 | vRestrict | Restricted areas for vias |  | 
Vias | Vias (through all layers) |  | 44 | Drills | Conducting through-holes |  | 
Unrouted | Airlines (rubber bands) |  | 45 | Holes | Non-conducting holes |  | 
Dimension | Board outlines (circles for holes) *) |  | 46 | Milling | Milling |  | 
tPlace | Silk screen, top side |  | 47 | Measures | Measures |  | 
bPlace | Silk screen, bottom side |  | 48 | Document | Documentation |  | 
tOrigins | Origins, top side (generated autom.) |  | 49 | Reference | Reference marks |  | 
bOrigins | Origins, bottom side (generated autom.) |  | 51 | tDocu | Detailed top screen print |  | 
tNames | Service print, top side (component NAME) |  | 52 | bDocu | Detailed bottom screen print |  | 
bNames | Service print, bottom s. (component NAME) |  |  |  |  |  | 

## Slide 18: Useful Layer Commands
“display <layer>” -- show the layer
“display -<layer>” – hide the layer
“display last” return to previous view
Click and hold the layer tool icon to get a list of present layers sets.
  Select “new…” to save the current view
  Then “display foo” to switch to the view named “foo”

## Slide 19: Layer Demo
The “Red board”
open /Users/swanson/UCSD/Teaching/17sp-190/QuadClass-Resources/Lecture\ Slides/Examples/ATmega128RFA1-DevBoard/ATmega128RFA1-DevBoard.brd

## Slide 20: Eagle Libraries

## Slide 21: Libraries
Libraries define the parts you can add to a PCB
Eagle libraries contain 3 different kinds of entities
  Schematic Symbols – The symbolic version of the part
  Package – The physical description of the part and how it should appear on the board
  Device – A combination of a package and a schematic

## Slide 22: Example: A Resistor
Schematic symbol
Has the standard resistor “zig zag”
Two ‘pins’
  Pas 1
  Pas 2
And place holders for documentation
  NAME – e.g. “R6”
  VALUE – e.g. “200Ohms”

## Slide 23: Example: A Resistor
Package
¼ Watt Yageo CFR Series through hole resistor
Two “pads” (through holes)
Silkscreen documentation
  Outline
  Name
Keep out area – Where other parts should not be!

## Slide 24: Example A Resistor
The Device
Maps the symbol to the package
There can be multiple “variants”
  Different packages
  Same symbol
  Same kind of device

## Slide 25: Layers In Packages
Packages have the same layers as boards.
For packages “t” means device side, “b” means opposite side.
If you put the devices on the back side of the board (i.e., “mirror” them), “t” and “b” will swap.

## Slide 26: Schematic Capture

## Slide 27: Schematics Goals
Determine what components your PCB will hold
Define the electrical connectivity between those components
Specify some metadata about the parts

## Slide 28: Schematic Example
open /Users/swanson/UCSD/Teaching/17sp-190/QuadClass-Resources/Lecture\ Slides/Examples/Myduino/Myduino.sch

## Slide 29: Eagle Pitfalls
Always edit schematics with your grid set to 0.1”
Wires/pins can look connected but not be.
  ‘Wiggle’ parts to make sure wires move with them.
  Check for the green dot.

## Slide 30: Board Layout

## Slide 31: Board Layout Goals
Mechanical constraints – Some things need to be in specific locations
Electrical constraints – Does the layout meet signal integrity/EM requirements
  Will digital interference mess up the antenna?
  Are decoupling caps near IC Supply pins?
  Keep the noisy power/ground for the motors away from the digital logic.
Correctness – things don’t overlap or hang off the board.
Ease of routing – Connected items should be physically close.
Make it pretty – you want a nice looking board
Potentially other, design-specific requirements

## Slide 32: Layout In Eagle
You can put things on the back of the board
  Use the “Mirror” tool.
You can also move around the reference designator
  Use the “squash” tool
You can rotate components with the rotate tool.

## Slide 33: Layout Demo
open /Users/swanson/UCSD/Teaching/17sp-190/QuadClass-Resources/Lecture\ Slides/Examples/Myduino/Myduino.sch

## Slide 34: The Three Ways to Route
Manual
  You can do anything you want (including things you shouldn’t)
Auto router
  Fully-automatic routing, subject to constraints that you can set.
“Follow me”
  Assisted manual routing. The router will enforce the constraints you set.
  Subject configurable cost functions.
  More control.

## Slide 35: Manual Routing Demo

## Slide 36: Auto Router
Mixed reputation
  It can’t do everything
  Sometimes it does a bad job
  When it works, it’s great.
Net classes (“Edit->Net Classes…”)
  Lets you set parameters for different kinds of nets (mostly width and clearances)
Lots of parameters to mess around with
  Optimization phases
  Routing grids
  Effort levels
  Concurrency
  Staged routing
  Checkout the Eagle Manual

## Slide 37: Follow Me Router Demo

## Slide 38: Auto Routing Demo

## Slide 39: Commands for Routing
“Auto;” – run the auto router (leave off the “;” to configure the router.
“Ripup;” – unroute signals
“Show <thing>” – Highlight a net or part

## Slide 40: Electrical Rules Check
This checks for common problems in schematics.
Run it!

## Slide 41: Design Rules Check
Checks that your board layout meets design requirements for manufacturing.
  Distance between traces and traces, traces and vias, etc.
  Trace width
  Etc.

## Slide 42: CAM Layers (Gerber files)
Eagle layers are for design.
CAM layers are for manufacturing
  “Gerber” files are for lithographic steps
  Drill files are for drilling holes.
Each CAM layers corresponds to one layer of the resulting board
  Top silk screen (.PLC)
  Top solder mask (.STC)
  Top metal (.TOP)
  Inner metal layers
  Bottom metal (.BOT)
  Bottom solder mask (.STS)
  Bottom silk screen (.PLS)
One drill file specifying where all the pads, vias, and mounting holes are located and their diameters (.DRD)
Other files too, depending on the manufacturing process
  Solder paste stencil
  Assembly drawings

## Slide 43: The CAM Processor
The CAM Processor generates CAM files
The exact configuration for the gerber files varies by board house
  Should the board outline be in every layer?
  Which format should the files be in (there are many)
  Should the back side layers be mirrored?

## Slide 44: CAM Setup
To prepare Gerbers for a particular board house, you need CAM setup files (*.cam for Eagle)
This specifies how to generate each layer the board house needs.
See example in Button and Light Tutorial.

## Slide 45: CAM Demo

## Slide 46: Checking Your Gerbers!
Eagle can’t display Gerber files itself
You need a 3rd party tool
  See the Button and Light tutorial for recommendations
You should always check your Gerbers!
  Eagle has bugs (I assume)
  You may have misconfigured something
  You may have put something in the wrong layer.

## Slide 47: Gerber Viewer Demo

## Slide 48: DFM Checks
You should also run a “design for manufacturing” (DFM) check on your Gerbers, if possible
Freedfm.com will do this for you.

## Slide 49: FreeDFM Demo

## Slide 50: The Lab
Use Eagle to design a simple schematic and board.
Run it through the tool flow.