## Slide 1: Designing Packages, Symbols, and Devices

## Slide 2: PCM Assembly
https://youtu.be/gu0v8lfLcKg?t=3m59s
https://youtu.be/2qk5vxWY46A?t=2m28s

## Slide 3: TODO
Add slides for:
  SMD vs Through holes
  Eagle PAD/SMD terminology.
  Flow chart/illustrations of assembly process.
  Anatomy of solder joint (showing miniscis)
  Side view of board + paste + component.
  Problems with IMU pads being in accessible.

## Slide 4: Part Sizes

## Slide 5: PCB Libraries
To use a part on a PCB, you need a library entry for it
  Physical/mechanical information for the board
  Logical/electrical information for the schematic
  Mapping between the two
  Metadata
A well designed library, will make your life much, much easier.
There are lots of libraries are the internet
  Some are good, some are bad, some a poor match for what we need.

## Slide 6
Package
Symbol
Device Pin Mapping
Physical part

## Slide 7: PCB Libraries: Packages
Mechanical description of the part
Electrical connections (i.e., pads and SMDs)
Other things: “keepouts”, mounting holes, documentation, labels etc.
Generic packages: e.g., 0805 Resistor
Specific packages: e.g., Atmegat128RF

## Slide 8: PCB Libraries: Symbols
Schematic representation of the component
Electrical connection points – “pins”
Generic symbols: resistors, capacitors, etc.
Specific symbols: e.g., Atmega128RF
Documentation, labels, etc.
Organized for ease of use and readability

## Slide 9: PCB Libraries: Devices
Devices map between
  1 symbol
  >=1 packages
For each package, the device maps the schematic pins to the package pads/SMDs.
Metadata
  “attributes” -- E.g., Manufacturer, part number, etc.
  Name prefix for reference designators -- e.g, the “R” in R1, R2, etc.
  Does it have a “value” (e.g., a resistor’s value is it’s resistance, but a microcontroller doesn’t have a value)

## Slide 10: Device Example: LED
One Symbol
Many Packages

## Slide 11: Devices in Eagle