## Slide 1: Demos
Show PWM signal changing duty cycle
Show flyback
  Effect of diode
  Show effect on power supply noise
Show filter on pwm line
  Effect of resistor and capacitor on PWM
  Show output of FET
  Show affect of filter on power supply noise

## Slide 2: Lab 5: The IMU, The Gimbals, and the Motor

## Slide 3: The Inputs and Outputs
Gimbals – How they work and how to read them.
Brushed Motors – How they work and how to drive them.
The IMU – microcontroller and IMU communicate.
The serial display, LEDs, etc. – Communicating with the pilot.

## Slide 4: Gimbals

## Slide 5: Controlling the Quadcopter
Standard RC “transmitters” have two sticks
  Left: throttle and yaw
  Right: pitch and roll
  This is called “mode 2” It’s different in Europe where they use “mode 1”
Yaw, pitch, and roll are spring-loaded to return to neutral
Throttle stays where you put it.

## Slide 6: The Gimbals
Each stick is a “gimbal”
  a mechanism, typically consisting of rings pivoted at right angles– The dictionary on my Mac

## Slide 7: Anatomy of a Gimbal
Two potentiometers measure X and Y movement of the stick.
Potentiometer – A variable voltage divider
  As the slider’s movement changes the resistance from A and W and W and B.
  The voltage at W is proportional to the position of the gimbal.
In reality, the resistances are always > 0, so W never reaches VCC or GND.
Our gimbal
  Frsky PR10
  Total resistance: 2.4KOhms
  Rated voltage: 5V

## Slide 8: Reading the Gimbals
The red board board has several analog input pins
analogRead(int pin)
  Takes a voltage between GND and Vcc and maps it to 0—1024
Check the schematic for the remote to see which pins are attached to which gimbals
    https://github.com/NVSL/Quadcopter-Remote

## Slide 9: Brushed DC Motors

## Slide 10: Brushed Motors

## Slide 11: Construction

## Slide 12: Construction (Rotor)

## Slide 13: Construction (Stator)

## Slide 14: Operation

## Slide 15: Operation

## Slide 16: Operation

## Slide 17: Operation

## Slide 18: Operation

## Slide 19: Flyback
Opening S1 makes M1 an inductor
  Drives up voltage M1-
  Can destroy the switch
  Can cause current to back to power supply.
  Causes noise on power supply.
This is called “fly back”
Adding a diode relieves the problem.

## Slide 20: Control
How would you control your motor’s speed?
  Speed ∝Voltage ∝Current
So, vary the input voltage
Generating varying voltages is non-trivial
  You need an digital-to-analog converter
Really, we just need the average voltage to vary

## Slide 21: Pulse-width Modulation (PWM)

## Slide 22: Selection
Free Speed:100 rpm
Stall Torque:8.6 in-lbs
Stall Current:2.6A
Free Current:0.18A
Specifications at 7.2V

## Slide 23: Our Motor Circuits

## Slide 24: PWM in Arduino
The red board board has several analog output (PWM) pins
analogWrite (int pin)
  Takes a value, x, between 0 (off) and 255 (on) and sets the duty cycle to x/255.

## Slide 25: I2C

## Slide 26: Inter-Integrated Circuit (I2C) Bus Interface AKA: Two Wire Interface (TWI)

## Slide 27: Brief History
Designed in 1982 by Philips Semiconductor (now NXP)
1992 - First public Spec released
Since 2006 no licensing fees are required
Widely adopted technology

## Slide 28: Why I2C?
Pins are precious!
  They take up space
  More pins  More expensive microcontrollers
  Adding pins is hard
    Might need a new microcontroller (if a larger, compatible one is available)
    Significant board changes
Performance is often not that important
So
  Use the minimum number of pins
  Run them at relatively low bit rates.

## Slide 29: Applications
Connecting to all kinds of small, slow peripherals
  Reading Configuration data from various devices (Memory, PCI cards)
  Accessing ADCs and DACs
  Reading from Real-time clocks
  Reading hardware monitoring devices (Fan speed, CPU Temperature, Accelerometers)
  Controlling power supplies for various system components
  GPIO expanders
  Many, many others

## Slide 30: I2C Bus Architecture
Two signals
  SCL – Serial Clock (used for coordination and timing)
  SDA – Serial Data (used for data and control signaling)
Up to 1008 peripherals
  1 or more “masters” that initiate communication on the bus
  Up to 127 “slaves” that masters communicate
Bit rates
  100 KHz (Standard mode)
  400 KHz (Fast Mode)
  3.4 MHz (High speed mode)
  1 MHz (Fast Mode Plus)
  5 MHz (Ultra fast mode)

## Slide 31: I2C Addressing
Each slave on an I2C bus has a unique address.
  Most use 7 bit addresses (we discuss this here)
  An extended 10-bit version also exists
The addresses usually fixed or only partially configurable
  E.g. Only the least-significant bit of the address for the IMU is settable. So you can only have two of these IMUs on one bus.
  Different devices will have different numbers of settable and fixed bits.
  You can’t mix components arbitrarily on the bus

## Slide 32: I2C Protocol - Full Xfer
Philips I2C Bus Specification
Start

## Slide 33: I2C Protocol - Full Xfer
Philips I2C Bus Specification
Address
R/W

## Slide 34: I2C Protocol - Full Xfer
Philips I2C Bus Specification
Data

## Slide 35: I2C Protocol - Full Xfer
Philips I2C Bus Specification
Stop

## Slide 36: The Serial LCD Display

## Slide 37: Display Text on the Remote
The LCD display on the remote is connected to the second serial port on the redboard
The LCD_library provides a nice interface for writing to it
  Docs here: http://playground.arduino.cc/Code/SerLCD

## Slide 38: Other Components

## Slide 39: Status LEDs
The remote has 3 status LEDs (D3, D4, D5) in the upper left of the control board.
They are useful for letting you know when the quad is armed, etc.
Use digital_write() to control them.

## Slide 40: Buttons
The remote has 2 buttons (B1, B2) for your use.
Use digital_read() to see if they are pressed.

## Slide 41: Pots
The remote has 2 potentiometers (TM1, TM2)
Use analog_read() to get their value.

## Slide 42: Lab Tasks
Use everything
  Install IMU library. Read values from IMU.
  Read the values from the gimbals.
  Display things on the serial display.
  Drive a motor.
  Turn the indicators on and off.
  Read values from the pots.
  Use the buttons to do something
Build a remote-controlled motor
  Stand alone red board drives motor.
  Remote control reads gimbals and transmits value to run motor at.
  This is the basic frame work for your quadcopter and remote firmware.