## Slide 1: Lab 1: Printed Circuit Boards: Layers, Layers, Layers

## Slide 2: Eagle Trick: The Command Line
You can type commands to Eagle. For some things it’s a huge help
Type “help <command>” to get help
There’s a command for each of the tools in the tool palette.
Useful commands for routing
  Auto – run the auto router
  Ripup – unroute signals
  Show – Highlight a net or part

## Slide 3: PCBs are Made of Layers
Silkscreen – documentation labels
Metal – for making wires
Dialectric – insulation and structure
Solder mask – protective outer coating

## Slide 4: Metal Layers
The Metal layers for several components
  Conductive “traces” to connect components
  Pads for attaching/connecting components
N-layer boards have N metal layers
  N usually is 2,4,...
  Fewer layers  cheaper
Top and bottom layers are for mounting components and routing traces
Internal layers can serve several purposes
  Ground and power planes
  Other signal planes
  Internal routing layers

## Slide 5: Metal Layers (cont.)
Thickness is measured in oz per square foot.
Standard copper is 1oz
  About 0.034 mm
Thicker metal layers can carry more current

## Slide 6: Dielectric
The dielectric in the insulator between metal layers
Most PCBs use FR4
  “glass reinforced epoxy laminate”
  i.e., fancy fiberglass
  “FR” means “flame retardant”
Other specialized dielectrics are are available
  To support high speed circuits
  To manage thermal expansion

## Slide 7: Solder Mask
The solder masking is a polymer (plastic) coating on the top and bottom of the board
Solder does not adhere to it.
It serves several needs
  Protects the top and bottom metal from oxidation.
  Helps prevent solder bridges
Gives the board color
  FR4 is brown
  Solder mask comes in several colors.

## Slide 8: Silkscreen
It’s an opaque (usually) white epoxy or polymer
It provides documentation and markings
  References designators
  Part outlines
  Logos
  Serial numbers etc.

## Slide 9: Making Connections Between Layers
Plated holes connect metal layers.
  Drill a hole
  Electroplate it with copper
The plating attaches to metal that the hole passes through

## Slide 10: Pads and Vias
Vias are electrical connections
  Usually very small.
Through hole pads accommodate through-hole parts
Even larger, mounting holes are possible

## Slide 11: Designing Through-hole Pads
The diameter of the hole is smaller than the drilled hole
  You need to add about 0.1-0.3 mm to the desired, plated internal diameter to get the drill diameter

## Slide 12: Lots of Choices, in Theory
There are many, many choices when designing a PCB
We will get to make very few of them
Cheap, quickturn PCB manufacturers provide a standard setup. E.g.:
  FR4
  1oz copper
  2 or 4 layers
  A few colors

## Slide 13: Resources
Videos of PCB Manufacturing
  This one is very good and really thorough, but it’s too long to watch in class.
  https://www.youtube.com/playlist?list=PL8zP8UuDk8a0ZNWiteC-7PHx1HCeBY0qB
White paper about board stackups
  www.icd.com.au/articles/Stackup_Planning_AN2011_2.pdf

## Slide 14: Steps for Designing PCBs
Create/acquire a library of components
Assemble your schematic
Lay out the board
Perform design checks
Generate CAM files
Perform more design checks
Submit for manufacturing

## Slide 15: Units
Units
  We will mostly use mm in this class.
  1mm is about 40mils (39.3700787, actually)
  1in is 25.4 mm.
  Keep an eye on your units.
Exceptions
  Lots of tutorials, documents, etc. use mils (1/1000 of an inch) or inches.
  Breadboards and headers are typically 0.1” spacing (2.54mm)
Mars Climate Orbiter

## Slide 16: Designing with Layers
Eagle (and other board design tools) use layers to specify different types of information about a board. E.g:
  Where wires should go on each physical layer
  Where wires should not go on each physical layer
  Documentation
  Mechanical information
Eagle defines 52 layers by default
‘t’ prefix means top.
‘b’ prefix means bottom (displayed mirrored)

## Slide 17: Eagle Layers
Top | Tracks, top side |  | 27 | tValues | Component VALUE, top side |  | 
Route2 | Inner layer |  | 28 | bValues | Component VALUE, bottom side |  | 
Route3 | Inner layer |  | 29 | tStop | Solder stop mask, top side (gen. autom.) |  | Design
Route4 | Inner layer |  | 30 | bStop | Solder stop mask, bottom side (gen. Autom.) |  | Documentation
Route5 | Inner layer |  | 31 | tCream | Solder cream, top side |  | Tool guidance
Route6 | Inner layer |  | 32 | bCream | Solder cream, bottom side |  | 
Route7 | Inner layer |  | 33 | tFinish | Finish, top side |  | 
Route8 | Inner layer |  | 34 | bFinish | Finish, bottom side |  | 
Route9 | Inner layer |  | 35 | tGlue | Glue mask, top side |  | 
Route10 | Inner layer |  | 36 | bGlue | Glue mask, bottom side |  | 
Route11 | Inner layer |  | 37 | tTest | Test and adjustment information, top side |  | 
Route12 | Inner layer |  | 38 | bTest | Test and adjustment inf., bottom side |  | 
Route13 | Inner layer |  | 39 | tKeepout | Restricted areas for components, top side |  | 
Route14 | Inner layer |  | 40 | bKeepout | Restricted areas for components, bottom s. |  | 
Route15 | Inner layer |  | 41 | tRestrict | Restricted areas for copper, top side |  | 
Bottom | Tracks, bottom side |  | 42 | bRestrict | Restricted areas for copper, bottom side |  | 
Pads | Pads (through-hole) |  | 43 | vRestrict | Restricted areas for vias |  | 
Vias | Vias (through all layers) |  | 44 | Drills | Conducting through-holes |  | 
Unrouted | Airlines (rubber bands) |  | 45 | Holes | Non-conducting holes |  | 
Dimension | Board outlines (circles for holes) |  | 46 | Milling | Milling |  | 
tPlace | Silk screen, top side |  | 47 | Measures | Measures |  | 
bPlace | Silk screen, bottom side |  | 48 | Document | Documentation |  | 
tOrigins | Origins, top side (generated autom.) |  | 49 | Reference | Reference marks |  | 
bOrigins | Origins, bottom side (generated autom.) |  | 51 | tDocu | Detailed top screen print |  | 
tNames | Service print, top side (component NAME) |  | 52 | bDocu | Detailed bottom screen print |  | 
bNames | Service print, bottom s. (component NAME) |  |  |  |  |  | 

## Slide 18: Useful Layer Commands
“display <layer>” -- show the layer
“display -<layer>” – hide the layer
“display last” return to previous view
Click and hold the layer tool icon to get a list of present layers sets.
  Select “new…” to save the current view
  Then “display foo” to switch to the view named “foo”

## Slide 19: Layer Demo
The “Red board”
open /Users/swanson/UCSD/Teaching/18sp-190/QuadClass-Resources/Lecture\ Slides/Examples/ATmega128RFA1-DevBoard/ATmega128RFA1-DevBoard.brd

## Slide 20: Eagle Libraries

## Slide 21: Libraries
Libraries define the parts you can add to a PCB
Eagle libraries contain 3 different kinds of entities
  Schematic Symbols – The symbolic version of the part
  Package – The physical description of the part and how it should appear on the board
  Device – A combination of a package and a schematic

## Slide 22: Example: A Resistor
Schematic symbol
Has the standard resistor “zig zag”
Two ‘pins’
  Pas 1
  Pas 2
And place holders for documentation
  >NAME – e.g. “R6”
  >VALUE – e.g. “200Ohms”

## Slide 23: Example: A Resistor
Package
¼ Watt Yageo CFR Series through hole resistor
Two “pads” (through holes)
Silkscreen documentation
  Outline
  Name
Keep out area – Where other parts should not be!

## Slide 24: Example: A Resistor
The Device
Maps the symbol to the package
There can be multiple “variants”
  Different packages
  Same symbol
  Same kind of device

## Slide 25: Layers In Packages
Packages have the same layers as boards.
For packages “t” means device side, “b” means opposite side.
If you put the devices on the back side of the board (i.e., “mirror” them), “t” and “b” will swap.

## Slide 26: The Lab
Use Eagle to design a simple schematic and board.
Run it through the tool flow.
https://sites.google.com/a/eng.ucsd.edu/quadcopterclass/labs/lab-2-using-eagle

## Slide 27: Eagle Lint
lint:
  Tool to check coding standards and other invariants about a computer system.
Eaglint will check your libraries, schematics
  Check for common problems
  Check for correctness
  Check for style
Also checks for other files in your repo
  Eaglint will tell you what it’s looking for.
  Pay attention.
Provides a workflow for me to review your designs and provide feedback.
To use
  Visit http://eaglint.nvsl.io
  You received a welcome email a couple of nights ago.

## Slide 28: Eagle Lint Process
Commit and push your changes to github
Submit your repo to Eaglint for a quick check
Submit your repo to Eaglint for a full check
If warnings/errors
  Fix and goto 1.
  Or justify them and goto 5
Submit for human review
If rejected
  Read comments; goto 1.
Else if accepted
  Goto next lab

## Slide 29: Grading on PCB Labs
The key to PCB design is attention to detail.
  Building a real board can take 4 months.
  If you make a mistake, it takes 4 months to fix.
    Contrast to software: just recompile and rerun!
  Don’t make any mistakes! Check your work!
Grading for PCB labs
  A “perfect” score is 10 points
  You start out with 15 points.
  Every time you submit a design to Eaglint, you lose a point.
  Every time you submit a design for human review Eaglint, you lose a point.
  You must complete the labs.
”Quick checks” are free.