## Slide 1: Schematic Design Reviews

## Slide 2: Attention to Detail
Getting a PCB to work means getting nothing wrong
You won’t have time for a respin, so we get one shot
You have to get everything right if we want to end up with a flying quad copter.
It’s called hardware for a reason.

## Slide 3: Design Review Process
Every device in our library and every schematic will be reviewed by one other person
  Fill in REVIEWER attribute on the device
  If you review a part, you are just as responsible for errors as the original designer.
If you really want your quadcopter to fly, you should review everything yourself.
Do not be afraid to call out problems.
Do not take problems that other people identify in your work personally. They are helping you.

## Slide 4: Design Review Process (Cont.)
Reviewers must be steadfast, picky, and demanding
  Do not accept hand waving!
  If you are not sure, ask someone else.
  You are all doing the same design, so there’s lots of expertise around.
The reviewer should do the review on their own and then meet with the designer to ask questions.
Make sure to allocate enough time for this meeting – 30min at least.
It is not the designer task to convince the reviewer that their design is correct. The reviewer must convince themselves, one way or the other.

## Slide 5: Design Reviews for Devices
Designing packages, symbols, and devices is a well defined task, determining whether its correct is relatively easy.
The designer should provide all the necessary materials
  They should all be in your github repo.

## Slide 6: Design Review Checklist for Packages/Devices/Symbols
For the LEDs you selected
  Did the designer give you the correct data sheet?
  Did they design for the right package?
  Is the item available on Digikey?
Pad size and location
  Pad dimensions for surface mount parts
    Does the pad extend at least 1mm out from the side of the package, so its easy to solder?
    Does it otherwise match the manufactures recommendations?
Pin Numbers and Mapping
  Do the pins in the schematic symbol map to the right physical pins?
  Do the physical pins match what’s in the data sheet?
  Are you sure you understand how the drawings in the data sheet are oriented?
Silkscreen
  Does the silk screen show how the device should be oriented?
  Does it include a part outline in tPlace? It should.
Documentation
  Is there a bounding box in tKeepout?
  Did they set the prefix for the device?
    Resistors, R
    Capacitors, C
    Inductors, L
    Diodes,D
    Transistors,Q
    ICs,U
    Header pins, J
    Jacks & Plugs,J
    Switches,S

## Slide 7: Design Review Checklist for Packages/Devices/Symbols (cont)
Symbol
  Is the symbol a reasonable size?
Are the pins arranged in a sensible fashion?

## Slide 8: Design Reviews for Schematics
You are all building the same design, so you should be very familiar with what the other team’s design will do
It is not enough to look it over say it looks basically correct.
You need to check EVERYTHING!

## Slide 9: Design Review Checklist for Schematics
Documentation
  Are all the names and values visible?
  Is the schematic laid out nicely? Is it organized?
Connectivity
  Are all non-connected nets labeled?
  Are all pins on all parts connected? If not, why?
  Are all the grounds connected? Is there only one BAT_GND ground net and one GND net?
  Is each power pin attached to the right power supply?
  Is each ground pin attached to right ground?
  Are all the pins actually connected? Or do they just look connected? (drag parts around to see)
Functionality
  Does the schematic do what it’s supposed to?
  Why was the value of each resistors and cap chosen?
  Are the decoupling caps the right size?

## Slide 10: Grading
10 points possible for the reviewers
  You have four days to do the review.
  2 points off for each day late (don’t keep the other team waiting).
1 point off for each error you don’t find.
  If we find a bug later that you should have caught, you are responsible.