## Slide 1: Lab Hours
Monday 6-9
Thursday 12-2.
Thursday 3:30-5

## Slide 2: Lab 3: The IMU, The Gimbals, and the Motor
Due midnight, April 11th

## Slide 3: Topics
Analog Inputs – How the microcontroller measure the position of the gimbals
Brushed Motors – How they work and how to drive them.
I2C – How the microcontroller and IMU communicate

## Slide 4: I2C

## Slide 5: Inter-Integrated Circuit (I2C) Bus Interface AKA: Two Wire Interface (TWI)

## Slide 6: Brief History
Designed in 1982 by Philips Semiconductor (now NXP)
1992 - First public Spec released
Since 2006 no licensing fees are required
Widely adopted technology

## Slide 7: Why I2C?
Pins are precious!
  They take up space
  More pins  More expensive microcontrollers
  Adding pins is hard
    Might need a new microcontroller (if a larger, compatible one is available)
    Significant board changes
Performance is often not that important
So
  Use the minimum number of pins
  Run them at relatively low bit rates.

## Slide 8: Applications
Connecting to all kinds of small, slow peripherals
  Reading Configuration data from various devices (Memory, PCI cards)
  Accessing ADCs and DACs
  Reading from Real-time clocks
  Reading hardware monitoring devices (Fan speed, CPU Temperature, Accelerometers)
  Controlling power supplies for various system components
  GPIO expanders
  Many, many others

## Slide 9: I2C Bus Architecture
Two signals
  SCL – Serial Clock (used for coordination and timing)
  SDA – Serial Data (used for data and control signaling)
You can have many peripherals
  1 or more “masters” that initiate communication on the bus
  Up to 127 “slaves” that master communicates with
Bit rates
  100 KHz (Standard mode)
  400 KHz (Fast Mode)
  3.4 MHz (High speed mode)
  1 MHz (Fast Mode Plus)
  5 MHz (Ultra fast mode)

## Slide 10: Masters and Slaves
Masters
  Can initiate transfers
  Drives the SCL line
  Normally only one Master
Master
Slave
SCL
SDA
Slave
  Can’t initiate transfers
  Respond to the Master
  Up to 100+ slaves per bus
Notes: Engineers have weird terms for everything. Masters and Slaves. Zombie children, Victim blocks, Evicting cache lines etc.

## Slide 11: I2C Protocol - Start/Stop
The Start/Stop sequences are the only times SDA can toggle while SCL is high
All other toggling of SDA must be done with SCL low

## Slide 12: I2C Addressing
Each slave on an I2C bus has a unique address.
  Most use 7 bit addresses (we discuss this here)
  An extended 10-bit version also exists
  Low-order bit determines whether it is a read or a write.
The addresses usually fixed or only partially configurable
  E.g. Only the least-significant bit of the address for the IMU is settable. So you can only have two of these IMUs on one bus.
  Different devices will have different numbers of settable and fixed bits.
  You can’t mix components arbitrarily on the bus

## Slide 13: I2C Protocol - Full Xfer
Philips I2C Bus Specification
Start

## Slide 14: I2C Protocol - Full Xfer
Philips I2C Bus Specification
Address
R/W

## Slide 15: I2C Protocol - Full Xfer
Philips I2C Bus Specification
Data

## Slide 16: I2C Protocol - Full Xfer
Philips I2C Bus Specification
Stop

## Slide 17: I2C Speed
100 Kb/sec - Normal Operation
10 Kb/sec - Slow mode
400 Kb/sec to 3.4 Mb/sec - High Speed Modes

## Slide 18: Clock Stretching
Only Masters can send clock pulses
But Slaves can stretch the clock if needed
Slave stretching the clock
Clock

## Slide 19: Gimbals

## Slide 20: Controlling the Quadcopter
Standard RC “transmitters” have two sticks
  Left: throttle and yaw
  Right: pitch and roll
  This is called “mode 2” It’s different in Europe where they use “mode 1”
Yaw, pitch, and roll are spring-loaded to return to neutral
Throttle stays where you put it.

## Slide 21: The Gimbals
Each stick is a “gimbal”
  a mechanism, typically consisting of rings pivoted at right angles, for keeping an instrument such as a compass or chronometer horizontal in a moving vessel or aircraft. – The dictionary on my Mac

## Slide 22: Anatomy of a Gimbal
Two potentiometers measure X and Y movement of the stick.
Potentiometer – A variable voltage divider
  As the slider moves, the resistances between A and W and W and B change.
  If A is at Vcc and B is at GND, then the voltage at W is proportional to the position of the gimbal.

## Slide 23: Measuring the Gimbals
You need the analogread() function in arduino.
  https://www.arduino.cc/en/Reference/AnalogRead

## Slide 24: Brushed DC Motors

## Slide 25: Brushed Motors

## Slide 26: Brushed Motors

## Slide 27: Construction

## Slide 28: Construction (Rotor)

## Slide 29: Construction (Stator)

## Slide 30: Operation

## Slide 31: Operation

## Slide 32: Operation

## Slide 33: Operation

## Slide 34: Operation

## Slide 35: H-Bridge

## Slide 36: Flyback
When S1 is open after the motor has been running, M1 becomes a big inductor
  It will drive up the voltage on GND
  Potentially damaging/interfering with other parts of the circuit
This is called “fly back”

## Slide 37: Flyback

## Slide 38: Flyback Diode
Adding a diode, allows the current to loop around through the motor and eventually dissipate

## Slide 39: H-Bridge

## Slide 40: Control
How would you control your motor’s speed?

## Slide 41: Control
How would you control your motor’s speed?
  Speed ∝Voltage ∝Current
So, vary the input voltage
Generating varying voltages is non-trivial
  You need an digital-to-analog converter
Really, we just need the average voltage to vary

## Slide 42: Pulse-width Modulation (PWM)

## Slide 43: Selection
Free Speed:100 rpm
Stall Torque:8.6 in-lbs
Stall Current:2.6A
Free Current:0.18A
Specifications at 7.2V

## Slide 44: Our Motor Circuits

## Slide 45: Analog IO in Arduino
The red board board has several analog pins
analogRead()
  Takes a voltage between GND and Vcc and maps it to 0—1024
analogWrite ()
  Takes a value, x, between 0 (off) and 255 (on) and sets the duty cycle to x/255.