## Slide 1: Logistics
There is some problem with programming the red boards, Jorge is working on a fix.
If you are not registered yet, let me know so I can get you admitted.
Also if you did not get an invitation to the piazza group, let me know so you can get one.
  This is how we will broadcast information to you, so you need to be signed up.
One person dropped, but one person is here today who wasn’t on Tuesday.
Lab times: We have lab time on Thursday, but not Tuesday
  At least not reliably on Tuesday. There’s another class in here.

## Slide 2: Eagle: Layers, Libraries, Layout, and CAM

## Slide 3: Eagle Trick: The Command Line
You can type commands to Eagle. For some things it’s a huge help
Type “help <command>” to get help
There’s a command for each of the tools in the tool palette.
Useful commands for routing
  Auto – run the auto router
  Ripup – unroute signals
  Show – Highlight a net or part

## Slide 4: Layers
Eagle (and other board design tools) use layers to specify different types of information about a board. E.g:
  Where wires should go on each physical layer
  Where wires should not go on each physical layer
  Documentation
  Mechanical information
Eagle defines 52 layers by default
‘t’ prefix means top.
‘b’ prefix means bottom (displayed mirrored)

## Slide 5: Eagle Layers
Top | Tracks, top side |  | 27 | tValues | Component VALUE, top side |  | 
Route2 | Inner layer |  | 28 | bValues | Component VALUE, bottom side |  | 
Route3 | Inner layer |  | 29 | tStop | Solder stop mask, top side (gen. autom.) |  | Design
Route4 | Inner layer |  | 30 | bStop | Solder stop mask, bottom side (gen. Autom.) |  | Documentation
Route5 | Inner layer |  | 31 | tCream | Solder cream, top side |  | Tool guidance
Route6 | Inner layer |  | 32 | bCream | Solder cream, bottom side |  | 
Route7 | Inner layer |  | 33 | tFinish | Finish, top side |  | 
Route8 | Inner layer |  | 34 | bFinish | Finish, bottom side |  | 
Route9 | Inner layer |  | 35 | tGlue | Glue mask, top side |  | 
Route10 | Inner layer |  | 36 | bGlue | Glue mask, bottom side |  | 
Route11 | Inner layer |  | 37 | tTest | Test and adjustment information, top side |  | 
Route12 | Inner layer |  | 38 | bTest | Test and adjustment inf., bottom side |  | 
Route13 | Inner layer |  | 39 | tKeepout | Restricted areas for components, top side |  | 
Route14 | Inner layer |  | 40 | bKeepout | Restricted areas for components, bottom s. |  | 
Route15 | Inner layer |  | 41 | tRestrict | Restricted areas for copper, top side |  | 
Bottom | Tracks, bottom side |  | 42 | bRestrict | Restricted areas for copper, bottom side |  | 
Pads | Pads (through-hole) |  | 43 | vRestrict | Restricted areas for vias |  | 
Vias | Vias (through all layers) |  | 44 | Drills | Conducting through-holes |  | 
Unrouted | Airlines (rubber bands) |  | 45 | Holes | Non-conducting holes |  | 
Dimension | Board outlines (circles for holes) *) |  | 46 | Milling | Milling |  | 
tPlace | Silk screen, top side |  | 47 | Measures | Measures |  | 
bPlace | Silk screen, bottom side |  | 48 | Document | Documentation |  | 
tOrigins | Origins, top side (generated autom.) |  | 49 | Reference | Reference marks |  | 
bOrigins | Origins, bottom side (generated autom.) |  | 51 | tDocu | Detailed top screen print |  | 
tNames | Service print, top side (component NAME) |  | 52 | bDocu | Detailed bottom screen print |  | 
bNames | Service print, bottom s. (component NAME) |  |  |  |  |  | 

## Slide 6: Useful Layer Commands
“display <layer>” -- show the layer
“display -<layer>” – hide the layer
“display last” return to previous view
Click and hold the layer tool icon to get a list of present layers sets.
  Select “new…” to save the current view
  Then “display foo” to switch to the view named “foo”

## Slide 7: Layer Demo

## Slide 8: Eagle Libraries

## Slide 9: Libraries
Libraries define the parts you can add to a PCB
Eagle libraries contain 3 different kinds of entities
  Schematic Symbols – The symbolic version of the part
  Package – The physical description of the part and how it should appear on the board
  Device – A combination of a package and a schematic

## Slide 10: Example: A Resistor
Schematic symbol
Has the standard resistor “zig zag”
Two connections
  Pas 1
  Pas 2
And place holders for documentation
  NAME – e.g. “R6”
  VALUE – e.g. “200Ohms”

## Slide 11: Example: A Resistor
Package
¼ Watt Yageo CFR Series through hole resistor
Two pads (through holes)
Silkscreen documentation
  Outline
  Name
Keep out area – Where other parts should not be!

## Slide 12: Example A Resistor
The Device
Maps the symbol to the package
There can be multiple “variants”
  Different packages
  Same symbol
  Same kind of device

## Slide 13: Layers In Packages
Packages have layers too, but not all of them
  E.g. no inner metal layers
For packages “t” means device side, “b” means opposite side.
If you put the devices on the back side of the board, “t” and “b” will swap.

## Slide 14: Board Layout

## Slide 15: Board Layout Goals
Mechanical constraints – Some things need to be in specific locations
Electrical constraints – Does the layout meet signal integrity/EM requirements
  Will digital interference mess up the antenna?
  Are decoupling caps near IC Supply pins?
  Keep the noisy power/ground for the motors away from the digital logic.
Correctness – things don’t overlap or hang off the board.
Ease of routing – Connected items should be physically close.
Make it pretty – you want a nice looking board 
Potentially other, design-specific requirements

## Slide 16: Layout In Eagle
You can put things on the back of the board
  Use the “Mirror” tool.
You can also move around the reference designator
  Use the “squash” tool
You can rotate components with the rotate tool.

## Slide 17: Layout Demo

## Slide 18: The Three Ways to Route
Manual
  You can do anything you want (including things you shouldn’t)
Auto router
  Fully-automatic routing, subject to constraints that you can set.
“Follow me”
  Assisted manual routing. The router will enforce the constraints you set.
  Subject configurable cost functions.
  More control.

## Slide 19: Manual Routing Demo

## Slide 20: Auto Router
Mixed reputation
  It can’t do everything
  Sometimes it does a bad job
  When it works, it’s great.
Net classes (“Edit->Net Classes…”)
  Lets you set parameters for different kinds of nets (mostly width and clearances)
Lots of parameters to mess around with
  Optimization phases
  Routing grids
  Effort levels
  Concurrency
  Staged routing
  Checkout the Eagle Manual

## Slide 21: Auto Routing Demo

## Slide 22: Follow Me Router Demo

## Slide 23: Commands for Routing
“Auto;” – run the auto router (leave off the “;” to configure the router.
“Ripup;” – unroute signals
“Show <thing>” – Highlight a net or part

## Slide 24: CAM Layers (Gerber files)
Eagle layers are for design.
CAM layers are for manufacturing
  “Gerber” files are for lithographic steps
  Drill files are for drilling holes.
Each CAM layers corresponds to one layer of the resulting board
  Top silk screen (.PLC)
  Top solder mask (.STC)
  Top metal (.TOP)
  Inner metal layers
  Bottom metal (.BOT)
  Bottom solder mask (.STS)
  Bottom silk screen (.PLS)
One drill file specifying where all the pads, vias, and mounting holes are located and their diameters (.DRD)
Other files too, depending on the manufacturing process
  Solder paste stencil
  Assembly drawings

## Slide 25: The CAM Processor
The CAM Processor generates CAM files
The exact configuration for the gerber files varies by board house
  Should the board outline be in every layer?
  Which format should the files be in (there are many)
  Should the back side layers be mirrored?

## Slide 26: CAM Setup
To prepare Gerbers for a particular board house, you need CAM setup files (*.cam for Eagle)
This specifies how to generate each layer the board house needs.
See example in Button and Light Tutorial.

## Slide 27: CAM Demo

## Slide 28: Checking Your Gerbers!
Eagle can’t display Gerber files itself
You need a 3rd party tool
  See the Button and Light tutorial for recommendations
You should always check your Gerbers!
  Eagle has bugs (I assume)
  You may have misconfigured something
  You may have put something in the wrong layer.

## Slide 29: Gerber Viewer Demo

## Slide 30: DFM Checks
You should also run a “design for manufacturing” (DFM) check on your Gerbers, if possible
Freedfm.com will do this for you.

## Slide 31: FreeDFM Demo