## Slide 1: The PID Controller

## Slide 2: What is PID?
Make a system follow a set point
“Proportional, Integral, Derivative”
A brief history:
  1788 - James Watt’s flyball governor (P)
  1837 - Louis Molinié hydraulic regulator (PI)
  1857 - H.N. Throop marine engine governor (PD)
  1868 - Maxwell gives theoretical basis
  1911 - Elmer Sperry, ship steering (PID)

## Slide 3: Control Theory
Making a physical system do what you want
“Open loop” and “closed loop”
Open loop - cannot see the system’s output
  Motor controllers
  LCD/LED/CRT screens
  Some ICBMs
Closed loop - Can see output, make corrections
  Autopilot
  GPS guided munitions
  Our quadcopter

## Slide 4: Closed loop control
PID is the most common closed loop controller
Proportional: Directly against error
Integral: Remembers error over time
Derivative: Dampens response to avoid oscillations

## Slide 5: Example
https://sites.google.com/site/fpgaandco/pid

## Slide 6: PID on the Quadcopter
3 separate controllers
PID set point is from user

## Slide 7: Pitfalls of PID
Integral term “Windup”
  One solution: turn it off unless we’re close
Derivative noise: beware of vibrations
Error term with vibration
Derivative term causes your system to go insane
  Solution: low pass (but not too much)
3. Tweaking PID values
  Know more about the system (auto tuners do this)

## Slide 8: Better than PID?
Better tweaking of parameters
  Knowing the whole transfer function helps
LQR (Linear Quadratic Regulator)
  Optimizes parameters for multiple outputs
  Available in Maple, MATLAB
But you have to know the system’s equations

## Slide 9: Questions